## Slide 1
Global timing FREQUENCY pulse train: 50 % duty cycle
Timing method 1
Counting trigger pulse
Move
Move
Advantages:
By choosing the amount of ticks before the counting trigger pulse one could ensure that the stage has completed movement and is motionless before actual acquisition of counts.
Disatvantages:
No photon counting while stage is moving.
Freq: 1000 * (1/(TimePPixel in ms + 0.1 ms))
TimePPixel in ms
Photons are counted during this time
X# of Ticks of 80 MHz Timebase << 0.1 ms
Move
Move
Move
Move
Move
Move
Move
Move

## Slide 2
Global timing TICKS pulse train: High time = TimePPixel in ms, low time arbitrary
Timing method 2
Move
Move
Move
Move
Move
Move
Move
Move
Move
Move
Photons are counted during this time
Advantages:
Extremely simple, no separate counting trigger needed.
Potentially less photons are ‘lost’. Although I am not convinced this is the case.
Disatvantages:
You are never sure of the ‘location’ of photons because the stage moves while photons are counted. But all depends on how much resolution you want/is possible at all.